Notes:
Target = Sample + Target combination, each are tracked separately
Launch Mapping_job for each sample
Start
Flag targets which are finished by
NumMapped <= oldNumMapped
Build Mapping results file (txt)
Add SplitReads job before exiting
Mapping_job
1 per sample
Load mapping results file
Iterate over targets
generate temp folder + fastq
Add Assembly job
Populate assemblies list
Launch CheckFinished with list of assemblies
SplitReads_job
1 per sample
Start assembly and check that it finished
Report assembly finished (or monitor job finished)
Count incomplete assemblies, if == 0
Add Concat job
Else add CheckFinished job
Assembly_job
1 per target
CheckFinished_job
1 per sample
If Target is finished
call Finish job, pass target
Else
Combine and rename contigs from all Targets, write to new targets.fasta
Add Mapping_job
Concat_job
Finish_job
Rename and add contigs to Sample_assemblies.fasta
Add statistics to Sample_statistics.tsv

---
Global “config” structure:
config = {}
reference=targets.fasta
numcycles=1
verbose=True
mapper=blat
nprocs=10
format=fastq
Samples = {}
Sample1 = {}
PE1 = FileName
PE2 = FileName
SE = FileName
Sample2 = {}
….
Global Folder Structure
TopLevel
ARC_config.txt ← Created by user
working_sample1 ← Created by setup() in __init__.py
targets.fasta ← Created for sample specific targets after the first iteration
idx ← contains the bowtie2 index if using bowtie2, created by mapper.py
target1 ← created by splitreads()
PE1
PE2
SE
assembly
finished ← created by the assembler when it finishes
...
Progress_Report
mapping_stats.tsv
additional files
Results
SampleN_contigs.fasta
SampleN_targetM_contigP ← name generated by Concat/Finisher
SampleN_target_statistics.tsv
read_map structure:

---
Additional Notes:
Read IDs
read IDs for PE reads might have old/new Illumina format, or be from some other technology.
We always need “1:2:3:4:5#0/1” format for Newbler to identify the PE reads
Current Solution:
all reads are split on “/” and the first portion kept, this value is used for the key in the SE and PE index files, and is what bowtie2 will output in the SAM files (note that bowtie2 does not split on #).
blat will output the full read name up to the first space and treats all reads as SE. The psl parser currently will strip off the